## Slide 1: LP Optimization: Industrial Cogeneration Operation
MATH 7205-Fall 2020
Joshua Galloway

## Slide 2: Presentation Outline
  Introduction
    Cogeneration Plant Operation Overview
  Problem Statement
    Fitting to Constrained Optimization Paradigm
  Process Model and Constraints
    Process Model
    Process Constraints via Mass Balances and Equipment Limits
    Objective Function via Energy Balance
    Canonical Form
  Results
    LP Optimization
    Solution Slightly Off LP Optimization Solution
  Conclusion

## Slide 3: Introduction
  Cogeneration Plant:
  Also called Combined Heat and Power (CHP)
  Produce Superheated Steam of Varying Pressures to Supply Industrial and Other Processes
  Steam is Produced By Large Industrial Boilers from Combustion of Fuels
    Biomass (Saw Dust, Bark, Corn Cobbs, Peanut Shells….)
    Fossil Fuels (Natural Gas, Fuel Oils, Coal)
  Steam is Generated at Higher than Required Pressure and Then Stepped-Down Through A Steam Turbine Generator to Produce Electrical Power
Kendall Square Cogeneration Station

## Slide 4: Introduction
  Header System:
  Equipment
    Distribution Headers
    Industrial Boiler (Steam Producer)
    Turbine Generators
    Condenser
    Pressure Reducing Valves
    Steam Vent Valve
  Superheated Steam Enters Turbine and Is Run Across Fins to Rotate a Coil of Wire In a Magnetic Field Producing Current
  TG1 has 2 Sets of Fins (called generating sections)
  TG2 has 3 Sets and a Condenser

## Slide 5: Problem Statement
  Physical System Requirements and Optimization:
  Mass Balance
    Steam Flows at All Nodes (Headers and Forks in Path) Must Sum to Zero
  Energy Balance
    Energy (Enthalpy Flows) must Sum to Zero at all Nodes
  Process Requirements
    Steam Users Must Receive Required Steam
    Equipment Design Limits Must be Obeyed or the Equipment will Fail
  Optimization:
    Choose the Best Path for Steam to Supply all Users and Obey Equipment Limits While Producing the Most Electricity Possible
Steam Pipe Failure, New York; Hydroelectric Turbine Failure, Russia

## Slide 6: Process Model and Constraints

## Slide 7: Process Model and Constraints

## Slide 8: Process Model and Constraints
Energy Balance for Objective Function

## Slide 9: Results
LP Solution:
J23 is Most Efficient so TG’s are Loaded to Send Max Steam Through to Condenser
An Overall Excess of Steam is Produced, So Vent is Open
Low Press Extraction is at Max so F_LP PRV is Open

## Slide 10: Results
Slightly Off LP Solution:
Steam Moved From Condenser to Vent
Slight Redirection of Extractions and PRV’s
Results in Loss of ~1 MW
Worth ~ $400K per year

## Slide 11: Conclusion
  We Saw…
  Introduction
    Cogeneration Plant Operation Overview
  Problem Statement
    Fitting to Constrained Optimization Paradigm
  Process Model and Constraints
    Mass and Energy Balances Used to Produce LP Canonical Form
  Results
    LP Optimization and Comparison
    LP Solution Roughly $400k More Production per Year
  Demo and Questions?